Project co-financed by EU

SUPPLY CONTRACT FOR EUROPEAN

UNION EXTERNAL ACTIONS

N° 1

financed from the EU General Budget

Gospodarska škola Čakovec,

Public institution

Vladimira Nazora 38, 40 000 Čakovec, Croatia

VAT: 38837480958

("The Contracting Authority"),

of the one part,

and

<Full official name of Contractor>

[Legal status/title]

[Official registration number]

[Full official address]

[VAT number], (“the Contractor”)

of the other part,

have agreed as follows:

CONTRACT TITLE

supply contract of equipment for hydroponic cultivation

# Identification number IPA4.1.3.1.03.02.c05

# Article 1	Subject

1.1	The subject of the contract shall be the supply, manufacture, delivery, installation, commissioning, maintenance, after-sales service of the following supplies:

In lots:

| LOT 1-GRUPA 1 : Građevinski radovi za izgradnju plastenika tipa "MULTIPLA" |
| --- |
| dim:1.lađe= | širina |  | dužina | br.lađa Š10m= | 1 | Ppvršina UKUPNA= | 400 m² |
|  | 10 | x | 40 |  |  |  |  |
| Dimenzije TEHNOLOŠKOG PROSTORA= | 5,5 | x | 10m |
| Komunikacijske staze po objektu= | širina | x | dužina |
|  | 2 m |  | 15 m |
| dimenzije bazena za floating kom= | 3 | 8 | x | 4 |  |
| dimenzije bazena za floating kom= | 1 | 7 | x | 4 |  |
| Lokacija: ČAKOVEC |
| ZEMLJANI RADOVI | Jed.mjere | Kom. |  |
| 1. | Iskolčenje objekta i geodetsko snimanje kod planiranja terena i iskopa temeljnih stopa broj temeljnih stopa kom =48 | kpl | 1 |  |
| 2. | Strojno skidanje humusa d=20-30 cm sa odlaganjem iste kraj objekta | m3 | 100 |  |
| 3. | Dovoz i razastiranje šljunka ili zemlje s grubom izvedbom padova | m3 | 60 |  |
| 4. | Strojno niveliranje i uvaljavanje zemlje i šljunka a prema padovima objekta i po projektu. | m2 | 400 |  |
| 5. | Strojni iskop rupa za temeljne stope u terenu 3-4. kategorije sa odvozom iskop.materijala pokraj objekta. Stope su dim. 40×40×50 cm; broj temeljnih stopa kom =48 | kom | 48 |  |
| 7. | Kopanje kanala 40x50cm za odvodnju procijednih voda i tehnoloških voda iz plastenika u terenu 3-4.kategorija sa odvozom viška iskopanog materijala pokraj objekta | m3 | 2 |  |
| 8. | Dobava pijeska i izvedba piješčane posteljice u padu, za polaganje kanalizacijskih cijevi | m3 | 0,4 |  |
| 9. | Zatrpavanje položenih kanalizacijskih cijevi i PE cijevi sa zemljom od iskopa. U cijeni uključeno i strojno nabijanje. | m3 | 1,4 |  |
| 10. | Dobava, razastiranje i fino planiranje pijeska u sloju d=5 cm kao podloge u plasteniku i valjanje iste za polaganje folije i betonskih ploča. | m2 | 400 |  |
| 11. | Strojni plitki iskop d=20cm za izvedbu AB komunikacijske staze i AB ploču tehnološkog prostora, sa odlaganjem zemlje kraj objekta. | m3 | 17 |  |
| 12. | Strojni plitki iskop zemlje d=20cm š=100cm za stazu oko plastenika, sa odlaganjem iste kraj objekta. | m3 | 11,2 |  |
| 13. | Dobava šljunka i razastiranje u sloju d= 20 cm kao podloge AB komunikacijskih staza š=2m i stazu oko plastenika š=1m. U cijeni uključeno i strojno nabijanje. | m3 | 28,2 |  |
| 14. | Strojni iskop zemlje 3. kategorije za upojni bunar , te dobava i polaganje betonske kanalizacijske cijevi Ø100cm. | kpl | 1 |  |
| 15. | Dobava šljunka i zatrpavanje upojnog bunara krupnim šljunkom. | m3 | 1,5 |  |
| BETONSKI RADOVI |  |  |  |
| 1. | Betoniranje temeljnih stopa podložnim betonom MB 15 d=10cm . Izvesti u padovima prema projektu. | m3 | 0,768 |  |
| 2. | Betoniranje temeljnih stopa, betonom MB 20 nakon postavljanja i centriranja konstrukcije plastenika. U cijenu uključena pomoćna oplata. | m3 | 3,072 |  |
| 3. | Izvedba A.B. temeljne grede 0,25×0,3×4m ,sa ugradnjom vodilice za klizna vrata. U cijeni uključen beton MB 20 i armatura. | m3 | 0,6 |  |
| 4. | Izvedba komunikac. staza š=2m i ploče u tehnološkom objektu od bet. Ploča dim. 50x50x5cm na pripremljenu podlogu te rubnjacima dim. 6x20x100cm , te fugiranje fuga .Podloga se izvodi od sloja šljunka i pijeska 0-4mm.Prema opterečenju se dodaje potrebna armatura. | m2 | 85 |  |
| 5. | Dobava i ugradnja betonskih rubnjaka dim: 6x25x100cm na podložni beton MB15 debljine 20cm, radi dobivanje čiste dubine bazena od 25cm.U cijenu uključeno prokopavanje šljunčane podloge za podložni beton i fino zaglađivanje istoga na stranama gdje naliježe folija bazena. | mt | 94 |  |
| 6. | Dobava i polaganja 200g. Geotextila kao zaštitne podloge folije za bazen. U cijni uračunati preklopi 15cm. | m² | 124 |  |
| 7. | Dobava i polaganje bazenske folije d=500mm UV zaštićene u svjetlo-plavoj boji. | m² | 175 |  |

| LOT 1-CASE 1: Construction work to build a greenhouse-type "multiple" dim: 1. arch= wid h x lenght Number of arches 10m= 1 Surface Total= 400 m² 10 40 Dimensions of technological space 5,5 x 10 m Communicational paths in the facility = width x lenght 2 m 15 m Dimensions of the pool for floating units= 3 8 x 4 Dimensions of the pool for floating units= 1 7 x 4 Location: ČAKOVEC A.) Clay works 1. Staking out the object and geodetical scanning by planning the field and dig of basic foot Number of basic foots units = 48 set 1 2. Taking off humus by a machine d=20-30 cm with disposal by the object m3 100 . Admitting and shedding of boulder or clay with rough performance of downfall m3 60 4. Tilting and rolling clay and boulder to downfalls of object according to the project m2 400 5. Machine dig of holes for basic foots in the field of 3-4. categorie with driving away digged material by the object. dim of the foots 40×40×50 cm Number of basic foot 48 units = units 48 7. Digging a canal 40x50cm for drainage of drainging and technological water from the greenhouse in the field 3-4.categorie with driving away surplus of digged material by the object m3 2 8. Supply of sand and performance of sand bed in the downfall, for laying down of canalizational pipes m3 0,4 9. Covering the canalizational pipes and PE pipes with digged clay. In price included machine tamping m3 1,4 10. Supply, shedding and fine planning of sand in layer d=5 cm as basecoat of the greenhouse and rolling in order to install the film and concrete panels. m2 400 11. Machine shallow excavation d=20cm to perform AB comunicational path and AB board of technological space, with laying down clay by the object. m3 17 12. Machine shallow excavation d=20cm w=100cm for the path around the greenhouse, with laying down by the object. m3 11,2 13. Supply and shedding of boulder in layer d= 20 cm as a basecoat AB of communicational paths w=2m and path around the greenhouse w=1m. In the price is also machine tamping m3 28,2 14. Machine excavation of clay 3. categorie for absorbing well , and supply and installation of concrete canalizational pipe Ø100cm. set 1 15. Supply of boulder and covering absorbing well with massive boulder. m3 1,5 CONCRETE WORKS 1. Concrete- work of the basic foots with concrete base MB 15 d=10cm . Perform in downfalls according to the project. m3 0,768 2. Concrete- work of the basic foots, with concrete MB 20 after installation and centring of construction of the greenhouse. In the price is accessary formwork. m3 3,072 3. Performance of A.B. basic balk 0,25×0,3×4m , with installation of driver for glideing door. In the price are concrete MB 20 and armature. m3 0,6 4. Performance of communicational paths width=2m and concrete board in technological object board dim. 50x50x5cm on prepared base and edges dim. 6x20x100cm , and fuguiring of fugues. Base consists layers of boulder and sand 0-4mm. According to burden necessary armature is added. m2 85 5. Supply and installation of concrete edges dim: 6x25x100cm on basic concrete MB15 20cm thick, in order to obtain clear depth of the 25cm pool. In the price is also digging through boulderly base for basic concrete and fine smoothing of it, on the side where lies the pool film. Peaces in m 94 6. Supply and laying down 200g. Geotextil as protecting bottom for film for the pool. In the price are included overlapping 15cm. m² 124 7. Supply and installation of the pool film d=500mm UV protected in light-blue color. m² 175 LOT 2-GRUPA2: PLASTENIK TIP PLASTENIKA RAVNI KOMADA 1 Dimenzije: 10,00 x 40,000 m Površina: 400,00 m2 Visina: 3,20 - 5,40 m Korak: 2,000 m Zatega: 3,60 m Red. br. materijal Jedinica mjere količina 1. Konstrukcija, lukovi, stupovi, razupore, zatege, ankeri kpl 21,0 2. Pojačanja za lukove Pojačanje "V" kpl 21,0 3. Dijagonale, ukručenja, krovne kom 2,0 4. Dijagonale, ukručenja, bočne kom 16,0 5. Dijagonale, ukručenja, čelne om 8,0 6. Čelne stranice s vratima kom 2,0 2,0 x 2,86m, klizna,polik.10mm Obloga: polik.6mm 2,0x2,56m.,klizna, polik.10mm. kom 1,0 Obloga: folija – unutar ja pregrada 7. Aluminijski profil kutni, veliki m´ 34,0 8. Bočne ventilacije m´ 80 0 Sokl folija 1,0m dupli al. pr. 9. Motoreduktor za bočne ventilacije kom 4,0 0,18kW-0,25HP,1 os.do 50 m,1:309 10. Dodaci motoreduktora za bočne ventilacije kom 4,0 Fiksno polje za motored. h=2,20m Te eskopska osovina L=1,20m, h=2,20 kom 4,0 11. Automatika za bočne ventilacije Za 4 motored.-2 zone+anemomet. kom 1,0 12. Fiksno polje Polik.4 mm - za ravni plast.h=3,20m kom 6,0 13. Krovna Ventilacija Za dužine do 40 m m´ 40,0 14. Motoreduktor za krovne ventilacije 0,18kW-0,25HP, do 40m- MRA 63/5 os. kom 2,0 15. Automatika za krovne ventilacije Za 2 motored.-2 zone+anemomet. kom 1,0 16. Pokrov : dvostruka Patilux folija m2 1.386,0 17. Plastični profili m´ 314,0 18. Ventilator za napuhavanje duple folije Kompl.presost.i 2 b passa kom 1,0 19. Termogen za grijanje kao Combiterm 60E; Plamenik na plin kom 2,0 20. Dodaci za termogen Ovjesni pribor kom. 8,0 Dodatna cijev ko 2,0 Pribor za priključak termog. kpl. 2,0 Puštanje u rad termogena kpl. 2,0 21. Ostalo Spajanje motoreduktora i automatike elektromaterijal kpl 12,0 Konstrukcija za visoke kulture-cijev o40, spojnice, žica, španeri m2 200,0 Energetska zavjesa XLS 1 – 0% m2 650,0 Konstruk.za autom.zasjenjiv. sa sajlama m2 400,0 Mo oreduktor za zavjesu kom 2,0 Autom.sa lux sondom kom 2,0 Glavni razvodni ormar sa osiguračima i sklopkama kpl 2,0 22. Transport, špedicija, montaža i edukacija korisnika i sve marže LOT 2: GREENHOUSE Type of greenhouse FLAT UNITS 1 imensions: 10,00 - 40,000 m Surface: 400,00 m2 Height: 3,20 - 5,40 m Step: 2,000 m Brace: 3,60 m Number material Measure unit units 1. Construction, arches, piles, braces, anchers set 21,0 2. Support for the arches Support "V" set 21,0 3. Diagonals, bracing, roof units 12,0 4. Diagonals, bracing, side units 16,0 5. Diagonals, bracing,front units 8,0 6. Front sides with doors 2,0 x 2,86m, sliding, polik.10mm Overlay: polik.6mm units 2,0 2,0x2,56m.,gliding, polik.10mm. Overlay: film – inner paravan units 1,0 7. Aluminum profile corner, large m´ 34,0 8. Side ventilation Sokl film 1,0m dubble al. pr. m´ 80,0 9. Motorspeedreducer for side ventilations 0,18kW-0,25HP,1 os.do 50 m,1:309 units 4,0 10. Addition of motorspeedreducer for side ventilation Fixed field for motorspeedreducer h=2,20m units 4,0 Telescopical spindle L=1,20m, h=2,20m units 4,0 11. Automatism for side ventilation for 4 motorspeedreducer.-2 zones+anemomet. units 1,0 12. Fixed field Polik.4 mm - for flat greenhouse h=3,20m units 6,0 13. Roof ventilation lenght to 40 m m´ 40,0 14. Motorspeedreducer for roof ventilation 0,18kW-0,25HP, do 40m- MRA 63/5 os. units 2,0 15. Automatism for roof ventilation for 2 motored.-2 zone + anemomet. units 1,0 16. coverage : double Patilux film m2 1.386,0 17. Plastic profiles m´ 314,0 18. Ventilator for blowing doubble film Kompl.presost.i 2 bypassa units 1,0 19. Heat termogen as Combiterm 60E Gas burner units 2,0 20. Termogen addition suspension kit units 8,0 Additional pipe units 2,0 Termogen plugging kit set 2,0 activation of termogen set 2,0 21. Other Connecting motorspeedreducer and automatcs Electromaterial set 12,0 High cultures construction – pipe o40, connectors, wire, tensioners m2 200,0 Energetic curtain XLS 15 – 50% m2 650,0 Construction for autom.shading With sling m2 400,0 Motorspeedreducer for curtain units 2,0 Autom.with lux sonde units 2,0 Main dividing closet with security fuses And switches set 2,0 22. Transport, forwarding, montage and education of users and all margin Dvostruka folija koja će se koristiti za pokrivanje mora biti minimalnih karakteristika u skladu s standardima EN 13206, 2002: IZGLED I DIMENZIJE MJERA IZNOS METODA Nazivna debljina Mikron 200 ISO 4593 Širina M 1,5 – 14,00 ISO4592 Izgled standard 8.1 EN 13206 T lerancija nazivne debljine % +-5 ISO4593 Tolerancija širine % 0:+2 ISO4592 MEHANIČKA SVOJSTVA Prekidna čvrstoća do kidanja po dužini i širini Mpa >22 EN ISO 5 7-3 Izduženje do trenutka kidanja po dužini i širini % >600 Otpornost na udar leda padajuće brzine 20 m/s ravno cN >500 Int. Method (IO 82.4002) Otpornost na udar leda padajuće brzine 20 m/s savijeno cN >350 OPTIČKA SVOJSTVA Ukupna propusnost sunčevog svjetla (400-700nm) >88 EN 2155-5 Difuzija svjetla (% of PAR) <20 EN 2155-9 Valne dužine UV z ačenja (280-380nm) % >10 IR plastenički efekt >60 8.9 EN 13206 Relativna propusnost svjetla DA OSTALA S OJSTVA Specifična težina g/m2 186 In . Method Svojstvo varenja – ljepljenja DA Vrijeme trajanja E- 4 godine EN13206 Termogen za grijanje sa plamenikom na plin minimalnih kapaciteta: Termogen za grijanje Plamenik na plin kom 2,0 minimalnih kapaciteta: Snaga kW 60 toplinske učinkovitosti % 90 Snaga ventilatora kW 0,5 Kapacitet puhanja ventilatora m3/h 4900 Statički tlak Pa 60 Temperaturna razlika Co 35 Električni napon V 230/400 Polje primjene Co -20 do +50 Double film which will be used as covercoat minimum characteristics according to standards EN 13206, 2002: APPEARANCE AND DIMENSIONS SCALE AMOUNT METHOD Thickness Mikron 200 ISO 4593 Width M 1,5 – 1 ,00 ISO4592 Appearance standard 8.1 EN 13206 Tolerance thickness % +-5 ISO4593 Broadness tolerance % 0:+2 ISO4592 MECHANICAL CHARACTERISTICS Solidness till rupture by lenght and width Mpa >22 EN ISO 527-3 Prolongation till rupture moment by lenght and width % >600 Impedance to ice impact with falling speed 20 m/s straight cN >500 Int. Method (IO 82.4002) Impedance to ice impact with falling speed 20 m/s bended cN >350 OPTICAL CHARACTERISTICS Total penetration of sunlight (400-700nm) >88 EN 2155-5 Light difusion (% of PAR) <20 EN 2155-9 Wave lenght UV ray (280-380nm) % >10 IR greenhouse effect >60 8.9 EN 13206 Relative light penetration yes OTHER CHARACTERISTICS Specific weight g/m2 186 Int. Method Characteristic welling – glueing yes Duration time E- years EN13206 Heat termogen with gas burner minimum capacity: Heat termogen: greenhouse gas burner units 2,0 Minimum capacity: Power kW 60 Heating efficiency % 90 Power of ventilator kW 0,5 Blowing capacity of ventilator m3/h 4900 Static pressure Pa 60 Temperature difference Co 35 Electric voltage V 230/400 Field of use Co -20 do +50 LOT 3-GRUPA3: Specifikacija opreme za hidroponski i floating uzgoj povrća u plasteniku dim: 1 lađa 10 × 40 m ( P=400 m² ) i to 200 m²salata-floting i 200 m²paprika-hidroponija širine: 10m dužine: 40m Napomena : P= 400,00 m² Proračun dimenzioniran na bazi - 3 biljke / mt jednoreda - 6 biljaka / mt dvoreda ukupan broj biljaka =459 Kom 2,3 kom/m² 1 sektora-navodnjavanja ukupna potrošnja vode= L/min= 15,3 0,918 m³/h A.) CENTRALNA STANICA ZA PRIPREMU OTOPINE 1. MINI Fertirigator mod kao DOSAJET mod A-2CDXM-70/20 (2,0kw), kontrola PHx1, kontrola ECx1, doziranje 2 tipa hranjiva + 1 kiselina, upravljanje sa 8 elektromagnetna ventila, bez fotoradiometrijske i drenažne sonde. kom 1 2. Drenažna sonda kom 1 3. Fotoradiometrijska sonda kom 1 4. Spremnik za otopinu od 2000 l sa poklopcem kom 1 5. Pumpa CPm 25/160B - 100L-30m-1,1kw kom 1 6. Cilindrični spremik za otopine 500L s poklopcem kom 3 7. Set za spajanje spremnika (filter,ventil,spojnice i flex. cijevi) kpl 3 8. Filter ø1 " ( 120 mesh ) kom 1 9. Filter ø1 1/2 " ( 120 mesh ) kom 1 10. Elektromagnetni ventil 1" / 24V kom 1 11. Kuglasti ventil Ž-Ž 1 "-PVC kom 4 12. Spojna obujmica za DOZEJET Ø32x1" kom 2 13. Spojni elektro materijal paušal 1 14. Spojni, pričvrsni i brtveni materijal paušal 1 B.) RAZVOD UNUTAR PLASTENIKA 1. Kuglasti ventil Ž-Ž 1 "PVC kom 2 2. Elektromagnetni ventil 1" / 24V kom 1 3. PE cijev ø 32 PN 4 m 40 4. PEHD-PE80 cijev ø 32 PN 6 m 10 5. PE-M spojnica 32x1" kom 6 6. PE koljeno ø 32 kom 4 7. PE spojnica ø 32 kom 1 8. PE "T" ø 32 kom 1 9 PE čep ø32 kom 1 10. PE obujmica 32x3/4" jednostrana kom 5 11. PE-PN10 koljeno M-Ž 3/4" kom 5 12. Ventil RME C/M ø 20×3/4" kom 5 13. PE cijev ø 20 PN 4 crno/bijela m 90 14. Ventil RPP C/C ø 20 kom 5 15. Kapaljka "Junior" CNL - utokompenz. 2 L/h om 51 16. Kapaljka "Junior" CNL - autokompenz. 4 L/h sa razdjelnikom kom 204 17. Spojna cijev ø 3/5 mm-.ECOVAR-crna m 275 18. Nosač kapilare pvc kom 459 19. PE-PN4 spojnica ø 20 kom 2 20. Bušač cijevi kom 1 1. Spojni, pričvrsni i brtveni mater jal paušal 1 C.) OPREMA ZA POLAGANJE PRESADNICA 1. Podna folija crno bijela 0,1 mm m2 210 2. "Bomat" ploče 100 x 20 x 7,5 cm (za dvored) kom 68 3. "Bomat" ploče 100 x 15 x 7,5 cm (za jednored) kom 17 4. "Bomat" kocka 10x10x6,5 cm - 2 čepa kom 210 5. "Bomat" kocka 7,5x7,5x6,5 cm - 1 čep kom 53 6. Čep za "Bomat" kocke kom 567 7. Kanalice od polipropilena dim.7,5 x 30 x7,5 cm ( žičani držači nisu u cijeni ) m 90 8. Poc.prirubnica ø60 a ispust kanalice kom 5 9. Podložni stiropor d=15mm , š=165mm m 90 10. Roler za povezivanje i polaganje rajčice kom 459 11. PVC kopča za vezanje rajčice ( 5/1 ) pak.=1000kom paket 2 D.) CIJEVI ZA ODVODNJU PROCIJEDNE OTOPINE 1. Kanalizacijska cijev ø 160 sa račvama m 12 E.) OPREMA ZA FLOATING 1. Centrifugalne pumpe od nehrđajućeg čelika,15 m³/h s 1,2 bar-0,75KW, s dijelom usisa i potisa, dijelom električnog upravljanja i izbornom sklopkom ručno uključi-isključi. kom 4 2. Cijevi za distribuciju svježe vode za punjenje bazena PVC Ø32 PN16, kompletno sa spojnicama za spajanje na instalaciju autoklava i odvojcima sa zapornim ventilima Ø32 za svaki bazen. m 40 3. Usisne cijevi od PVC-a Ø 63 s odgovarajućim priključcima. m 40 4. Potisne cijevi od PVC-a Ø 63 s odgovarajućim priključcima. m 40 5. Sekundarnih cijevi kao češalj od PVC-a Ø 32 dugačkih 4,5 m s odgovarajućim rupama, kompletiranih s konzolama i spojnicama za spajanje na glavnu potisnu cijev. m 80 6. Elek romagnetni ventil 11/2" / 24V kom 4 7. Kuglasti ventil Ž-Ž 1 "-PVC kom 4 8. Venturijeve cijevi od PVC-a DN 25. kom 4 9. Mjerač kisika u vodi Mjerno područje 0-45 mg kisika/l vode Zasićenost % 0-300 Temperatura ˚C 0-50 kom. 1 10. Spojni, pričvrsni i brtveni materijal paušal 1 F.)Transport, špedicija, montaža i edukacija korisnika i sve marže LOT 3: Specifications of equipment for hydroponic and floating growth of vegetables in the greenhouse dim: 1 arch 10 × 40 m ( P=400 m² ) 200 m²letucce-floating and 200 m²peppers-hydroponics width: 10m lenght: 40m Instruction : P= 400,00 m² Budget is based on - 3 plants/ mt in one line - 6 plants / mt in two lines Total number of plants =459 pieces 2,3 pieces/m² 1 sector-irrigation - totale usage of water= L/min= 15,3 0,918 m³/h A.) CENTRAL STATION FOR PREPARATION OFSOLUTION 1. MINI Fertirigator mod as DOSAJET mod A-2CDXM-70/20 (2,0kw), control PHx1, control ECx1, dosage 2 types of nutrition + 1 acid, management with 8 electromagnetic ventiles without fotoradiometrical and dreinage sonde. Unit 1 2. Dreinage sonde Unit 1 3. Fotoradiometrical sonde Unit 1 4. Reservoir for solution of 2000 l with the cap Unit 1 5. Pump CPm 25/160B - 100L-30m-1,1kw Unit 1 6. Cylindric reservoir for solutions 500L with the cap Unit 3 7. Set for connection of reservoir (filter,vent,connectors and flex. pipes) set 3 8. Filter ø1 " ( 120 mesh ) Unit 1 9. Filter ø1 1/2 " ( 120 mesh ) Unit 1 10. Electromagnetic vent 1" / 24V Unit 1 11. Ball vent Ž-Ž 1 "-PVC Unit 4 12. Connecting embracer for DOZEJET Ø32x1" unit 2 13. Connecting electromaterial Lump sum 1 14. Connecting, tightening and jointing material Lump sum 1 B.) Separation in the greenhouse 1. ball vent Ž-Ž 1 "PVC Unit 2 2. E ectromagnetic vent 1" / 24V Unit 1 3. PE pipe ø 32 PN 4 m 40 4. PEHD-PE80 pipe ø 32 PN 6 m 10 5. PE-M connector 32x1" Unit 6 6. PE knee cap ø 32 unit 4 7. PE connector ø 32 Unit 1 8. PE "T" ø 32 Unit 1 9. PE cap ø32 Unit 1 10. PE embracer 32x3/4" onesided Unit 5 11. PE-PN10knee cap M-Ž 3/4" Unit 5 12. Vent RME C/M ø 20×3/4" unit 5 13. PE pipe ø 20 PN 4 black/white m 90 14. Vent RPP C/C ø 20 Unit 5 15. Dropper "Junior" CNL - autokompenz. 2 L/h unit 51 16. Dropper "Junior" CNL - autokompenz. 4 L/h with divider unit 204 17. Connecting pipe ø 3/5 mm-.ECOVAR-black m 275 18. Carrier capilars pvc unit 459 19. PE-PN4 connector ø 20 unit 2 20. Pipe driller unit 1 21. Connecting, tightening and jointing material Lump sum 1 C.) EQUIPMENT FOR DEPOSIT OF OVERSEEDLING 1. Floor film black-white 0,1 mm m2 210 2. "Bomat" board 100 x 20 x 7,5 cm (for two lines) unit 68 3. "Bomat" board 100 x 15 x 7,5 cm (for one line) unit 17 4. "Bomat" cube 10x10x6,5 cm – 2 caps unit 210 5. "Bomat" cube 7,5x7,5x6,5 cm - 1 cap unit 53 6. Cap for "Bomat" cubes unit 567 7. Hollow tile of polipropilen dim.7,5 x 30 x7,5 cm ( wired holders arent in the price ) m 90 8. Poc. edger ø60 for hollow tile unit 5 9. Underlying styroform l=15mm , w=165mm m 90 10. Roller for bonding and deposit of tomatoes unit 459 11. PVC clutch for bonding tomatoes ( 5/1 ) pacagge.=1000 peaces package 2 D.) PIPES FOR DREINAGE OF SOLUTION 1. canalization pipe ø 160 pitchfork m 12 E.) FLOATING EQUIPMENT 1. Centrifugal pump of stainlessn steel,15 m³/h s 1,2 bar-0,75KW, with partial absorbation and push, partial electrical management and selective hand switch on/off. unit 4 2. Pipes for distribution of fresh water for filling the pool PVC Ø32 PN16, completely with connectors for connecting on instalation autoclave and extensions with cut-off vents Ø32 for each pool. m 40 3. Absorbing PVC pipes Ø 63 with attachments. m 40 4. Pushing PVC pipes Ø 63 with attachment m 40 5. Secundary pipes as PVC comb Ø 32 long 4,5 m with holes, completed with consoles and connectors to connect on main pushing pipe. m 80 6. Electromagnetic vent 11/2" / 24V unit 4 7. Ball vent Ž-Ž 1 "-PVC unit 4 8. Venturiuses PVC pipes DN 25. unit 4 9. Measure divice for oxigyen in the water Measurement area 0-45 mg oxiygen/lwater saturation % 0-300 Temperature ˚C 0-50 unit 1 10. Connecting, tightening and jointing material Lump-sum 1 F.)Transport, forwarding, montage and educacation of users and all margins LOT 4-GRUPA 4: Sijačica i oprema sijačice Sijačica mora biti dostupna kao samostojeći stroj s mogućnošću uključenja u proizvodnu liniju. Bubanj mora imati mogućnost sijanja linija za sjetvu u širokom rasponu, biti jednostavan za rukovanje i promjenu sjemena iz jedne vrste u drugu. Kontrolna ploča mora omogućavati jednostavno upravljanje proizvodnjom s jednog mjesta. Bubanj i valjak dibbler se moraju lako mijenjati za različite vrste sjemena i pritom ne zahtijevati posebne alate. Uz to mora imati još slijedeće tehničke karakteristike i mogućnosti: Ostale opcije Priključak za veći kapacitet zraka silicijske mlaznice sapnice za multi sjeme Uz osnovni stroj sijačicu isporučuje se i kompresor koji pokreće radni proces, a koji mora zadovoljiti minimalne tehničke karakteristike: max.tlak (bar): 11 napajanje (V/Hz): 400/50 kapacitet zraka (litr/min.): 514 elektromotor : 3 fazni (400 V) rezervoar zraka (litara): 200 polu-automatska sijačica s pneumatskim sustavom, pogodna za svaku vrstu saća i sjemena, bez obzira da li je golo ili peletirano, komplet sa automatskim diblerom kompaktni stroj automatska ladica automatsko sjetva automatski dibbler promjenljiva brzina proizvodnje varijabilni tlak vakuma za sjeme podtlak - tlak za čišćenje mlaznica 6 kompleta mlaznice različitih veličina kućište je sastavljeno iz čeličnog ormara s vratima za internu pohranu. značajke automatskog sustava s mogućnošću indeksiranja dibblera i sjetvenog mehanizma automatsko pokretanje saća nakon sjetve, vakumsko usisavanje sjemenja sa tzv. Venturi sistemom linija aspirator za preostalo sjeme pneumatski vibrator sjemena kod spuštanja u tanjur - saće komplet dizni 0,20-0,25-0,30-0,35-0,40,0,45-0,50-0,60-0,70 kapacitet redaka/ sati do 1700 max dimenzije saća u koju se spušta sjeme u mm 600x400 kapacitet zraka l/min 120 max Uz sijačicu tražimo i 2 različita kompleta za sjetvu sjemena kao U tip R84 (komada 1) i R209 (komada 1). LOT 4: Sowing machine and equipment The sowing machine must be available as selfstanding machine with the possibility of joining to production line. The drum must have a possibility of insemination lines for in broad range, be simple to use and changing the seeds from one species to the other. Control board must secure simple management with production from one place. The drum and the roller dibbler must be easily shifted for different species of seeds without the neecesity for other special tools. Also, it must have these characteristics Other options connection for larger air capacity silicium jets spray nozer for multi seed By the basic machine the compressor that runs working process is also being delivered, and has the following minimal technical characteristics: max.pressure (bar): 11 voltage (V/Hz): 400/50 air capacity (litr/min.): 514 electroengine: 3 phase (400 V) air reservoar (liters): 200 semi-automatic sowing machine with pneumatic system, pogodna for every kind of comb and seeds (naked or pelleting), in set with automatic dibbler compact machine automatic drawer automatic insemination automatic dibbler shiftable speed of production variable pressure of seed vacum subpressure for cleaninig the jets 6 complets of jet in different sizes case consists of steel closet with doors for inner storage characteristics of automatic system with the possibility of indexation of dibbler and sowing mechanism automatic start of comb after insemination vacuum suction of seeds with Venturius line system aspirator for seed left overs pneumathic vibrator of seeds at deposit in the comb complete lifting 0,20-0,25-0,30-0,35-0,40,0,45-0,50-0,60-0,70 capacity of lines/hours to 1700 max dimensions of combs for the deposit of seeds mm 600x400 air capacity l/min 120 max By sowing machine, we are procuring 2 various sets for sowing seeds as U type R84 (1 unit) i R209 (1 unit). LOT 5-GRUPA 5: Visokotlačni perač Mora imati minimalne karakteristike : snaga 2,5kW; protok 500 l; tlak 120 bar-a; topla voda 90o C . |  |
| --- | --- |

| LOT 5: High pressure washer | Minimum characteristics required: |
| --- | --- |
|  | power 2,5kW; flow 500 l; pressure 120 bar-a; warm water 90o C . |

After-sales services for Lot no. 1,2,3,4,5,

| List requested after-sales services maintenance response time availability of spare parts availability of maintenance | The duration of after-sales services 1 year 3 days 5 years 5 years |
| --- | --- |

The place of acceptance of the supplies shall be:

In 1,2,3,4,5 lots deliver at/to

Gospodarska škola Čakovec

Školska ekonomija Mihovljan

40 000 Čakovec

the time limits for delivery shall be 7-15 h each working day and the Incoterm applicable shall be DDU.  The implementation period will last 120 starting from day of commencement of the Contract and ending on the day of issuance of the certificate of Provisional Acceptance. The implementation period will include delivery period of 90 days.

1.2	The Contractor shall comply strictly with the terms of the Special Conditions and the technical annex.

# Article 2	Origin

The supplies must originate in a Member State of the European Union, European Economic Area (EEA), candidate country or a country beneficiary of the IPA programme.  Contractors must present proof of origin to the Grant Beneficiary no later then when the first invoice is presented, for equipment and vehicles of a unit price of purchase of more then 5 000 EUR.

Failure to comply with this condition may result in the termination of the contract.

The origin of the goods shall be determined according to the Community Customs Code or the international agreements to which the country concerned is a signatory.

# Article 3	Price

3.1		The price of the supplies shall be that shown on the financial offer (specimen in Annex IV). The total maximum contract price shall be 81 285 € or 596 632 KN.

3.2 		Payments shall be made in accordance with the General and/or Special Conditions (Articles 26 to 28).

# Article 4	Order of precedence of contract documents

The contract is made up of the following documents, in order of precedence:

- the contract agreement;

- the Special Conditions

- the General Conditions (Annex I);

- the Technical Specifications + Technical Offer (Annex II+III)

- the budget breakdown (Annex IV);

- specified forms and other relevant documents (Annex V);

# The various documents making up the contract shall be deemed to be mutually explanatory; in cases of ambiguity or divergence, they shall prevail in the order in which they appear above.

Done in English in two originals, one original being for the Grant Beneficiary and one original being for the Contractor.

| For the Contractor | For the Grant Beneficiary |
| --- | --- |
| Name: |  | Name: Sabrina Blajda |  |
| Title: |  | Title: dipl.ing. |  |
| Signature: |  | Signature: |  |
| Date: |  | Date: |  |

# Footnotes

Where the contracting party is an individual.

Where applicable. For individuals, mention their ID card or passport or equivalent document – number.

Except where the contracting party is not VAT registered.

DDU (Delivered Duty Unpaid)  -  Incoterms 2000 International Chamber of Commerce - http://www.iccwbo.org/incoterms/id3040/index.html